## Slide 1: SUMO Simulation (a quick review)
Byron Mason

## Slide 2: Setup
Simple T junction
  No right turn on red
  Right turn on red
Four vehicle types
  pkw
  bus
  bike
  scooter
Traffic flows
  L15 to L13 and L18
  L14 to L16 and L18
  L17 to L13 and L16
L15
L13
L18
L14
L16
L17

## Slide 3: Setup
Vehicles are defined as follows

## Slide 4: Setup
Routes are defined as follows

## Slide 5: Setup
For each flow the number of vehicles is
  pkw (5)
  bus (1)
  bike (10)
  scooter (500)
Simulation is run for 600 seconds
Emissions model is used to output CO2, CO, HC, NOx, PMx and fuel consumption at every timestep (HBEFA3, HBEFA4)
Python script is used to add all of the emissions across all of the vehicles
Note emissions output from bike is 0.

## Slide 6: Simulation Results - Right turn on red
CO2 (mg) - 79153877
CO (mg) - 890638
HC (mg) - 56037
Nox (mg) - 149915
PMx (mg) - 32182
Fuel (mg) - 25483976

## Slide 7: Simulation Results - No right turn on red
CO2 (mg) - 81354980
CO (mg) - 915166
HC (mg) - 55975
NOx (mg) - 153109
PMx (mg) - 33939
Fuel (mg) - 26192613

## Slide 8: Simulation Results

## Slide 9: Simulation Results - Comparison
Results show up to 5% difference due to change in turn rules (PMx)
Results normalised due to large difference in magnitude across emissions species
Chart: Normalised Emissions Results
| CO2 (mg) | CO (mg) | HC (mg) | NOx (mg) | PMx (mg) | Fuel (mg)
Right on red | 0.97294 | 0.9732 | 1 | 0.97914 | 0.94823 | 0.97295
No right on red | 1 | 1 | 0.99889 | 1 | 1 | 1

## Slide 10: Simulation Results – Changing fleet composition
Number of vehicles in each class for each flow was changed whilst keeping the total number of vehicles the same.
No right turn on red was enforced
  Run 1: pkw (5), bus (20), bike (10), scooter (480)
  Run 2: pkw (100), bus (25), bike (10), scooter (380)
  Run 3: pkw (15), bus (100), bike (20), scooter (380)
  Run 4: pkw (380), bus (100), bike (20), scooter (15)

## Slide 11: Simulation Results
Interesting results since pkw(5), bus(1), bike(10), mbike(500) shows significantly lower emissions across all species (this was the case presented previously)
Chart: Normalised emissions over various fleet compositions
| CO2 (mg) | CO (mg) | HC (mg) | NOx (mg) | PMx (mg) | Fuel (mg)
pkw(5), bus(1), bike(10), mbike(500) | 0.16933 | 0.35822 | 0.26984 | 0.043845 | 0.36262 | 0.17203
pkw(5), bus(20), bike(10), mbike(480) | 0.70497 | 0.44482 | 0.79097 | 0.70592 | 0.83247 | 0.70571
pkw(100), bus(25), bike(10), mbike(380) | 0.9137 | 1 | 0.84998 | 0.82284 | 0.8305 | 0.91437
pkw(15), bus(100), bike(20), mbike(380) | 1 | 0.80401 | 1 | 1 | 1 | 1
pkw(380), bus(100), bike(20), mbike(15) | 0.96172 | 0.98026 | 0.90555 | 0.90687 | 0.87878 | 0.96193

## Slide 12: Simulation Results
pkw (15), bus (100), bike (20), mbike (380)

## Slide 13: Observations
Simulation shows sensitivity to fleet composition and turn rules which is a good start
The magnitude of the difference appears significant however some further validation of expected emissions levels should be investigated
Results obtained for fleet composition study are unexpected in that the first run shows significantly lower emissions which should be investigated. This could be due to low bus numbers. 1 in the first run compared with 20, 25, 100, 100 in subsequent runs

## Slide 14: Observations
Parameters of scooter vehicle class were changed to reflect Vietnamese driving style but this is currently not based on any observational data and likely therefore not a true reflection. Lane discipline behaviour for example doesn’t appear correct.
Simulation is quick to run through GUI but automation will help speed things up.

## Slide 15: Future Work
Need to develop code to automate simulation and results acquisition / processing.
Should also consider interface with MBC for simulation parameter setting and importing of simulation results for model creation.
Vietnamese driving behaviour needs to be considered and characterised in the simulation
Emissions classes selected for vehicles should be based on some level of fact
Need to incorporate some measure of how traffic is affected (beyond emissions) by input factors e.g. wait time
Traffic flow rates and fleet composition needs to be considered
It is not clear how SUM places the different vehicles in the simulation and this should be investigated

## Slide 16: Future Work
The simple T junction is a good starting example, but work should begin on characterising a real junction since behaviour is likely to be more complex
Fleet composition at real junction should be based on available evidence (or observation)
Need to consider which factors to include in screening experiment

## Slide 17: Notes – Vehicle Types
Vehicle types are fixed but may vary as more cars are brought into the fleet. This will likely reduce the number of scooters.
Vehicle type study is a prediction of what will happen in the future as a consequence of external factors and does not consider what can be done today in terms of road layout etc (internal factors)
Policy changes which are internal factors could incentivise the use of public transport over scooters
The study should perhaps focus on internal factors such as
  Traffic light timing
  Lane rules
There is a problem in creating a surrogate model of continuous vs discrete variables